GOA SHIPYARD LIMITED.

Shipbuilders, Shiprepairers & Engineers.

(A Govt. of India Undertaking – Ministry of Defence)

Vasco da Gama, Goa-403 802, India.

Notice no: J24/PK/SPS/Shotblasting		CIN no: U63032GA1967GO1000077

Expression of Interest  ( EOI ) from  suitable Indian  firms for operatinalisation of shot Blasting plant located in GSL Steel Preparation Shop ( SPS )

M/s Goa Shipyard Limited had Installed  a Shot Blasting & Priming Plant  in the year 1988 from UK. Over the years, efficiency of the plant has dropped and several features became non-operational. The said plant needs to be revamped by localizing (Indigenizing) and changing the mechanical parts, Priming section and its Pneumatic spraying mechanism, Blasting chamber, electrical Panels, etc for restoring the plant for complete efficient operation.

Following major issues are identified with the current Shot Blasting & Priming machine  and needs to be rectified:

A. Paint Spraying System

- Bottom paint spraying assembly is damaged and non-operational due to which plates are to be turned manually and conveyor to be reversed and then repainted which is time consuming process & labour intensive.

- Top paint spraying gun assembly is working, but spraying mechanism is covering more than the Steel plate area thus causing wastage of paint, since the control of paint spray mechanism adjustment for smaller width of steel plates is non-operational for past 3 – 4 years.

B. Shot blasting System

- 6 nos. of pneumatic valves controlling the operation of control cage for positioning of shots delivery is non-operational, due to which the shots are not delivered as per the required  plate width and the excess shots directly hits the blasting chamber tiles and securing dome nuts resulting in dislodging of tiles.

- The   broken tile pieces get jammed with the bottom spiral, rendering stoppage of the plant, thus leading to manual recovering of the shots from the bottom spiral.

- Tiles pieces to have Indigenous replacement and also to review securing arrangement to have longer life for securing dome nuts.

C. Dust separation

I. All 08 solenoid valves for dust separation are found to be defective and need replacement for smooth functioning of the Shot Blasting Machine.

D. Plate unloading/ loading systems

I. There are two Plate unloading/ loading systems. One is working and the other is not.  The one which is not working needs to be made operational. The scope includes overhauling/ renewal of gear box, motor and chain sprocket system.

II. Further, both loading and unloading systems need to be overhauled.

III. The external dust collection units need to be overhauled.

Interested firms may visit GSL to have a overlook of the machine. You may contact Mr. Prashant Kumar, DGM(SPS),GSL, Goa on e mail – prashant@goashipyard.com or on Mobile no. +91 9423311321.

An introductory letter for expression of Interest (EOI) along with requisite copies of certificates/ supporting documents may be forwarded by courier to aforesaid address and soft copy of the same be sent by e mail to prashant@goashipyard.com within 20 days of publishing of this advertisement for evaluation. Shortlisted firms will be intimated on further course of action.

GSL reserves the right to accept/ reject the firms who have responded to this EOI, without any financial or other liability to GSL and without assigning any reasons thereof.